## Slide 1: Degrees of displacement: The impact of household PV battery prosumage on utility generation and energy storage Kelvin Say & Wolf-Peter Schill

## Slide 2: Electricity customers are changing.
AEMO, 2018. 2018 Electricity Statement of Opportunities for the NEM.

## Slide 3: Derivation of customer value.
22c/kWh
7c/kWh
Retail usage charges/kWh:
Diminishing returns for additional PV capacity + eligibility considerations

## Slide 4: The value shifts with PV-battery prosumage.
22c/kWh
7c/kWh
PV and battery investments are intertwined
Batteries revalue excess PV generation (minus losses)
Prosumage adoption becomes a combined consideration of PV and battery capacity
Interaction with FiT eligibility
FiT incentives are “flipped”
* Assuming batteries only operate to maximise self-consumption

## Slide 5: Changing shape of residual network demand.
Batteries incentivise additional PV capacity
Declining minimum midday demand
Declining late-afternoon peak
Emerging residual morning peak
Increased morning to midday down ramping
Say, K., John, M. (Under revision). Shifting sands: Transitions in diurnal and seasonal demand arising from household PV battery adoption

## Slide 6: Changing shape of residual network demand.
Shifting into winter dominant demand
Say, K., John, M. (Under revision). Shifting sands: Transitions in diurnal and seasonal demand arising from household PV battery adoption

## Slide 7: A changing customer, a changing power sector.
With costs of battery systems declining and electricity prices rising,
what impacts could household PV-battery adoption have on the power sector?
Household investment simulation model
Utility-scale dispatch and investment model
Residual network demand
2030
2019 to 2030

## Slide 8: The case study.
Western Australia’s South West Interconnected System (SWIS) Network
Islanded network, currently unable to export elsewhere or curtail household PV
Significant wind and solar resources
Around 18 TWh of annual energy consumption with households consuming around 30%

## Slide 9: The research setup.
Customer
Household batteries only operate for “self-consumption”

## Slide 10: Data sources.
Input Parameters | Value | Source
Household underlying demand and generation (heterogenous) | 261 Sydney homes via half-hourly gross meter data 2012-13 | (Ausgrid)
Residential/utility PV cost projection curves | Scaled by 0.78 | (Solar Choice, GenCost 2018)
Residential/utility battery cost projection curves | Scaled by 0.73 | (Solar Choice, Schmidt et al. )
Retail usage tariff projections | 29c/kWh +4%pa (Synergy, ABS) | (Synergy, ABS)
Underlying network demand | SWIS operational demand 2012-13 | (AEMO)
Number of investing households | 500,000 | Forecasted number of PV installations (AEMO)
Other technology costs | Conventional, wind, hydrogen, biomass | (GenCost 2018)
Wind resource | Time-series | (AEMO)
Solar resource | Time-series average of household insolation data | (Ausgrid)

## Slide 11: The scenarios investigated.
We compare scenarios with varying FiT and RES shares to a counterfactual setting without prosumage.
FiTs at 0%, 25%, 50% of retail usage charge
Constrained RES share at 39%, 49%, 59%
2019
FiT @ 0%
FiT @ 25%
FiT @ 50%
2030
RES share @ 39%
RES share @ 49%
RES share @ 59%
Residual
network
demand
Residual
network
demand
Residual
network
demand
Residual
network
demand
Counterfactual (Reference)

## Slide 12: Various degrees of prosumage.
Higher FiTs discourage battery adoption and keeps households at the eligibility limit (5 kWP)
Lowering FiTs encourages battery adoption
Larger consumption households may exceed FiT eligibility limit
PV-only
PVB
PVB+
Annual Consumption

## Slide 13: Capacity impacts.
Reference (counterfactual) scenario
No PV battery investing households
More wind than utility PV capacity
Increased utility battery capacity as RES share rises

## Slide 14: Capacity impacts.
PV-only FiT50 scenario
Average 5 kWP with no batteries
Displacement in both utility PV and wind capacity
Wind capacity recovers as RES increases
Greater utility PV capacity displacement as RES increases
Further utility battery capacity added

## Slide 15: Capacity impacts.
PVB FiT25 scenario
Average 5.3 kWP + 5.9 kWh
Displacement in both utility PV and wind capacity
Wind capacity recovers as RES increases
Greater utility PV capacity displacement as RES increases
Little effect on utility battery capacity

## Slide 16: Capacity impacts.
PVB+ FiT0 scenario
Average 4.7 kWP + 8.7 kWh
Reduced displacement of utility PV capacity
Wind capacity recovers as RES increases
Greater utility PV capacity displacement as RES increases
Little effect on utility battery capacity

## Slide 17: Generation impacts.
Reference (counterfactual) scenario
No PV battery investing households
Wind is an increasingly important resource, higher capacity factor of wind means that wind contributes more to the generation mix
Coal has greatest reduction
OCGT, CCGT generally unaffected

## Slide 18: Generation impacts.
Slight coal enhancing effect

## Slide 19: Wholesale price impacts.
Commercial & industrial demand
Household demand
Average wholesale price
Commercial & industrial demand
500,000 non-prosumage households
500,000 prosumage households
Average wholesale price
?
?
?
Commercial & industrial demand
500,000 non-prosumage households
500,000 prosumage households
Average wholesale price
e.g. PVB FiT25 and 49% RES share
Late-afternoon peak prices fall
Mid-morning prices rise
Wholesale prices for non-prosumage also fall slightly
Cost of supply to C&I rises slightly

## Slide 20: Overall system cost effects.
Higher PV battery investment costs for customers leads to sub-optimal allocation of capital across the power sector

## Slide 21: Key findings.
Utility PV generally substituted by household PV capacity but less so as additional household batteries are installed
Wind power is less affected especially in scenarios with higher shares of renewables
Utility battery capacities are hardly substituted with household batteries operating to maximise self-consumption
Slight decrease in wholesale prices faced by non-prosumage households less so with prosumage households, while other consumers are slightly increased
Potential system benefits from more system-oriented household battery operation

## Slide 22
Date/Location | Presenter | Topic
Mon 24 Feb 11am Climate College | Craig Memery (Public Interest Advocacy Centre) | Industrial demand response (Victorian Clean Technology Fund Series)
Wed 26 Feb 11am Climate College | Prof Jörg Niewöhner (Humboldt University) | Human/Environment research for/in the anthropocene: A land-use perspective
Wed 4 Mar 11am Climate College | Felix Schenuit (University of Hamburg) | Governance of carbon dioxide removal in the European Union
Wed 11 Mar 11am Climate College | Violette Mouchaileh (AEMO) Tim Nelson (AEMC) | Regulatory support for industrial demand response (VCTF Series)
climatecollege.unimelb.edu.au/seminars
@climatecollege

## Slide 23: Effects on residual load duration curves (RLDCs)
RLDC:
Hourly total load minus variable renewable generation
Sorted in descending order
Note: the sorting changes between curves
Here: example for 49% RES share and FiT25

## Slide 24: Overall: prosumage leads to slightly flatter RLDC
Overall flatter RLDCs
Also slightly higher surplus generation
There are two effects:
More PV
Household batteries

## Slide 25: i) More PV
Effect of utility-scale PV

## Slide 26: i) More PV
PV capacity increases to prosumage capacity level, but dispatched as utility PV
“Belly of the duck”

## Slide 27: ii) Household batteries
Smooting effect of PV batteries on left and right-hand side

## Slide 28: ii) Household batteries
This effect is still visible if wind power is also considered

## Slide 29: Overall: prosumage leads to slightly flatter RLDC